## Slide 1: Introduction
Upamanyu Madhow
ECE Department
University of California, Santa Barbara

## Slide 2: 2 decades of wireless growth
Digital cellular is now global
  6B mobile phone subscribers today!
  Connects the most remote locations to the global economy
WiFi is pervasive and growing
  Huge growth in carrier and enterprise markets
  Huge potential in residential markets in developing nations
Technology is was converging
  MIMO, OFDM part of all modern standards
mmWave represents a fundamental disruption

## Slide 3: mm-wave: what’s different?
System goals: multiGbps wireless
Bandwidth no longer a constraint
Channel characteristics
  Sparse rather than rich scattering
The nature of MIMO
  Beamforming, diversity, multiplexing all different at tiny wavelengths
Signal processing at multiGbps speeds
  ADC is a bottleneck, OFDM may not be the best choice
Networking with highly directional links
So really, everything is different!

## Slide 4: Interdisciplinary approach is essential

## Slide 5: Example: NSF GigaNets project
Rodwell (UCSB)
Madhow (UCSB)
+
Buckwalter (UCSB)
Zheng (U. Chicago)
Circuits
Systems
Arbabian (Stanford)
Zhang (UCSD)

## Slide 6: The Opportunity
Technology and Applications

## Slide 7: The end of spectral hunger?
(freq, GHz)
55
60
65
USA
60 GHz: 14 GHz of unlicensed spectrum!
E/W bands: 13 GHz of semi-unlicensed spectrum
70
75
80
85
90
95
Bands beyond 100 GHz becoming accessible as RFIC and packaging
technology advances
70
Oxygen absorption
(ideal for short-range, multihop)
Recently opened up
No oxygen absorption
Longer range links, esp with no rain

## Slide 8: To put it in perspective
Equivalent spectrum
Conventional
Cellular
Original 7 GHz unlicensed
band at 60 GHz
Notes: FCC federal communications comission
Mmwave is not a new discovery..
These boxes in there shows that these spectrum are also been owned by people but haven’t been used widely…

## Slide 9: We now have a virtuous cycle
Mm-wave in silicon
Packaging advances
Unlicensed
Semi-unlicensed
WLAN, cellular,
backhaul, radar
Technology
Applications
Regulations

## Slide 10: Initial industry focus: indoor 60 GHz networks
WiGig spec/IEEE 802.11ad standard: up to 7 Gbps
Support for moderately directional links
32 element antennas that can steer around obstacles
www.technologyreview.com

## Slide 11: Progress due to push for WiGig
60 GHz CMOS RFICs
  WiFi-like economies of scale if and when market takes off
Antenna array in package (32 elements)
  Good enough for indoor consumer electronics applications
MAC protocol supporting directional links
  Good enough for quasi-static environments
  Does not provide interference suppression
  Does not scale to very large number of elements
Gigabit PHY
  Standard OFDM and singlecarrier approaches
  Does not scale to 10 Gbps at reasonable power consumption (ADC bottleneck)

## Slide 12: Now: mmWave for 5G
NEED EXPONENTIAL INCREASE IN
CELLULAR NETWORK CAPACITY
(without breaking the bank)
Driven by exponential growth in cellular data demand

## Slide 13: Industry consensus on the need for Cellular 1000X
Figure courtesy: Cisco
Figure courtesy:
Qualcomm
Figure courtesy:
Nokia
Notes: The thirst for mobile data will grow exponentially
Shannon’s law (nWlog(1+SNR))

## Slide 14: Mm-wave enables aggressive spatial reuse
Large arrays in small form factors
Directive links
Limited interference
Dense cells / much higher spatial reuse
32 x 32
8 x 8 cm2
Access
Backhaul
Terragraph
(WiGig repurposed)

## Slide 15: 1000X via mm-wave
Bandwidth (W)
Up to a few GHz
10-100X
Cell density (n)
High spatial reuse
100X
Spectral efficiency (SNR)
Directive antennas but higher noise figure
0.1-1X

## Slide 16: mm-wave comm: a snapshot

## Slide 17: In addition…mmWave commodity radar
Vehicular situational awareness
Gesture recognition
Designs constrained by cost, complexity and geometry
Very different from classical long-range military radar

## Slide 18: Challenges
(aka Research Opportunities)

## Slide 19: Must revisit all key concepts in wireless design
Revisiting channel models for tiny wavelengths
  Sparse, easily blocked
  Critical role of directionality
  Geometric rather than statistical view of MIMO
Revisiting signal processing architectures
  The ADC bottleneck
Revisiting networking
  Highly directional links change MAC design considerations
  Multi-band operation (e.g., 1-5 GHz and 60 GHz)
Revisiting radar
  Short-range geometry and hardware constraints
Inherently cross-layer even at the level of comm and estimation theory
  Node form factor, hardware constraints, propagation geometry

## Slide 20: Channel Modeling
Slides mostly due to: Maryam Eslami Rasekh

## Slide 21: Step 0: can we close the link?
Take-away from link budget
Low-cost silicon works for indoor links
Low-cost silicon also works for short outdoor links
(~100 meters)

## Slide 22: Is propagation on our side?
Can we attain the kind of system specs we want with technology compatible with the mass market?
  Link budget for indoor links
  Link budget for outdoor links (oxygen absorption)
CMOS power amps: sweet spot 0-10 dBm
SiGe power amps can go higher
Using antenna arrays, can we go far enough so it is interesting?

## Slide 23: Free space propagation
The simplest model for how transmit power translates to received power
Isotropic transmission  at range R, the power is distributed over
the surface of a sphere of radius R
Receiver antenna provides an aperture with an effective area for
catching a fraction of this power
If the transmitter uses a directional antenna:
Transmit antenna
gain
Receive antenna
aperture

## Slide 24: Relating gain to aperture
Aperture for an
“isotropic” antenna
Antenna gain = ratio of aperture to that of an isotropic antenna
Remarks
--For given aperture, gain decreases with wavelength
--Aperture roughly related to area  at lower carrier frequencies
(larger wavelengths) we need larger form factors to achieve
a given antenna gain

## Slide 25: Friis’ formula for free space propagation
Given the antenna gains:
For fixed antenna gains, the larger the wavelength the better
Given the antenna apertures:
For fixed antenna apertures (roughly equivalent to fixed form factors),
the smaller the wavelength the better, provided we can point the
transmitter and receiver at each other

## Slide 26: Applying Friis’ formula
Going to the dB domain:
More generally:
Plug in your
favorite model
for path loss
Free space path loss model gives us back the first formula:

## Slide 27: Link budget
Given a desired receiver sensitivity (i.e., received power),
what is the required transmit power to attain a desired range?
OR
what is the attainable range for a given transmit power?
Must account for transmit and receive directivities, path loss, and
add on a link margin (for unmodeled, unforseen contingencies)

## Slide 28: Link budget analysis
Receiver sensitivity: minimum received power required to attain
a desired error probability
(depends on the modulation scheme, bit rate, channel model,
receiver noise figure)
Link budget: Once we know the receiver sensitivity, we can work
backward and figure out the physical link parameters required
to deliver the required received power (plus a margin of safety)
Basic comm theory maps modulation & coding scheme to Eb/N0
requirement; we then need to map to received power needed
We can now design the physical link parameters: transmit and receive
antennas, transmit power, link range

## Slide 29: Receiver sensitivity
(noise power)
Receiver sensitivity (minimum receive power needed)

## Slide 30: Receiver sensitivity in dBm
We therefore obtain
How should we design the system to attain the desired RX sensitivity?
Need to relate transmit power to received power
At room temperature and for a bandwidth of 1 Hz, the noise power
equals -174 dBm
(for noise figure
of F dB)

## Slide 31: Numerical value of noise PSD
White noise arising from many devices in the receiver can be summarized into a single quantity Noise figure: tells us how big the PSD is with respect to a benchmark
Benchmark: thermal noise of a resistor with matched impedance at “room temperature”
Noise figure usually expressed in dB, and noise power can be computed as follows:
Power often expressed in dBm

## Slide 32: Example 60 GHz indoor link budget
4x4 antenna array at each end, 2 dBi gain per element
 14 dBi gain at each end
10 m range  free-space path loss is about 88 dB
2.5 Gbps link using QPSK and rate 13/16 code operating 2 dB
from Shannon limit
Receiver sensitivity = -71.5 dBm
Noise figure 6 dB
Transmit power with 10 dB link margin is only about -1.5 dBm!
( can use less directive antennas)

## Slide 33: Example 100 m outdoor 60 GHz link (backhaul, base-to-mobile)
Free space propagation loss increases by 20 dB
Oxygen absorption (16 dB/km) leads to 1.6 dB additional loss
Rain margin (25 dB/km for 2 inches/hr): 2.5 dB
Required transmit power goes up to 22.6 dBm
For 4x4 array, TX power per element is 10.6 dBm
(doable with CMOS, easy with SiGe)
EIRP = 22.6 dBm + 14 dBi = 36.6 dBm < FCC EIRP limit of 40 dBm
Using 10 m indoor link budget as reference

## Slide 34: What the link budgets tell us
60 GHz is well matched to indoor networking and to picocellular networks
  Oxygen absorption has limited impact at moderate ranges
  Heavy rain can be accommodated in link budget
  Moderate directivity suffices
  Electronically steerable links give flexibility in networking
  Low-cost silicon implementations are possible
For truly long range, need to avoid oxygen absorption
  64-71 (unlicensed), 71-76, 81-86 GHz (semi-unlicensed)
  Bands above 100 GHz
  Need very high directivity (can we steer effectively?)

## Slide 35: Step 1: Channel Characterization
Take-away
Sparse, geometrically predictable channels
Very different from statistical models used at lower frequencies

## Slide 36: Basics of channel modeling
Sum of propagation paths
  Free space propagation (LOS)
  Specular reflection
  Propagation through dielectric obstacles
  Diffraction and scattering
All these components are strong in conventional lower frequency bands (<6GHz) but in mmwave..?

## Slide 37: reflection

## Slide 38: Reflection
Plane wave traveling in homogenous environment
Electric permittivity
of vacuum
Relative permittivity
Magnetic permeability of vacuum
Relative permeability
(phasor)
constant phase plane
(wave front)
Magnetic permeability
Electric permittivity

## Slide 39: Reflection
Plane wave reflection and transition: Snell’s law
Speed of light in substance

## Slide 40: Reflection coeffs
Fresnel formula derived from Maxwell’s equations
  Depend on magnetic permeability and electric permittivity

## Slide 41: Reflection
Note: for normal surfaces perpendicular reflection coefficient is negative

## Slide 42: Reflection
Note: for normal surfaces perpendicular reflection coefficient is negative
and for parallel reflection we have:

## Slide 43: Reflection coeffs have mild freq dependence
Quasi-plane wave:
TX
RX

## Slide 44: Main freq dependence is from rough scattering
Reflection from rough surfaces: part of wave energy is scattered
Higher loss at higher frequencies (exponential)
(surfaces are rougher at shorter wavelengths)

## Slide 45: Roughness: 5 GHz vs 60 GHz
Surface roughness std deviation varies from 0 (e.g. glass) to a few mm
At low frequencies (f < 6 GHz, λ > 5 cm) most surfaces are smooth
At 60 GHz a surface with 0.6 mm roughness causes 5 dB of excess loss

## Slide 46
Take-away on reflections
One bounce path is usable
(typically 5-10 dB weaker than LoS)
Multi-bounce paths usually too weak to be useful
(bonus: less worry about interference)

## Slide 47: Blockage

## Slide 48: Propagation through dielectrics
Dielectric loss is result of resonance of particles with electromagnetic field – varies with frequency
Oxygen absorption (e.g. at 60 GHz) result of such resonance
Exponential decay with distance

## Slide 49: Propagation through dielectrics
Penetration loss increases exponentially with depth and frequency
x
Phase change
Attenuation
…

## Slide 50: Propagation through dielectrics
Example: relative permittivity of concrete
@ 5 GHz: εr = 4.8 – j0.6
@ 60 GHz: εr = 3.3 – j0.38
Loss of a 3 cm thick slab of concrete
@ 5 GHz:
@ 60 GHz:
How thick can a slab of concrete be for <10dB attenuation?
@ 5 GHz: 8.04 cm
@ 60 GHz: 8.8 mm
Mm-wave cannot propagate through obstacles

## Slide 51: Can we diffract around obstacles?
wavefront decomposition
for point source
wavefront decomposition
for plane wave
Need Huygen’s principle to understand this

## Slide 52: Huygens’ principle
If part of wavefront is blocked, contribution of that portion is lost

## Slide 53: Huygens’ principle
If part of wavefront is blocked contribution of that portion is lost
equivalent pattern of blocked sources
equivalent pattern of blocked sources

## Slide 54: Huygens’ principle
If part of wavefront is blocked contribution of that portion is lost
equivalent pattern of blocked sources
equivalent pattern of blocked sources
more of power reaching front of obstacle is lost

## Slide 55: Can mostly write off diffraction
Fresnel zone heuristic
Can’t diffract around human obstacles in picocells, for example

## Slide 56
Take-away on blockage
When a path is blocked, it’s blocked
(can’t burn through it, can’t diffract around it)
Must steer around obstacles

## Slide 57: OVERALL channel model

## Slide 58: Quasi-deterministic modeling
Example lamppost-to-lamppost link
LoS + single bounce reflections from side walls and road
Can vary lamppost heights and street width to get multiple realizations

## Slide 59: Basic ray tracing
Relative delays: compute using geometry
Path strength: reflection model, propagation distance, beam patterns
Relative phase: uniform (small path length differences cause large
phase differences)

## Slide 60: Sparse channel model
  Channel impulse response (gains account for TX and RX directivity)
Modeled as uniform over

## Slide 61: Sparse channel impulse response

## Slide 62: Easily extends to multiple antennas

## Slide 63
Example SIMO system: relative channel gains are
Phase difference:
Need to be careful with relative phases

## Slide 64: Take-away on millimeter wave channel Sparse and geometrically predictable

## Slide 65: Take-way on millimeter wave channel Sparse and geometrically predictable
Do measurements back this up?

## Slide 66: Measurements on UCSB campus
Measurements at different locations on campus
16-element phased array @ 60 GHz
Steers beam in horizontal plane (azimuth)
TX
RX
TX angle
(azimuth)
RX angle
(azimuth)
Facebook Terragraph node
(Narrow vertical beam  ground reflection not present on typical measurements)

## Slide 68: Received power: angular profile
Reflection from window on right wall

## Slide 69: Consistent with 2 rays
Reflection from window on right wall
Receiver sidelobes
Transmitter sidelobes

## Slide 70
RX

## Slide 71: Another 2-ray channel
Reflection from wall near receiver

## Slide 72: Reflected path for 2nd ray
RX

## Slide 73: We expect only the LoS path here
RX
TX

## Slide 74: 1-ray model

## Slide 75: Other measurement campaigns show similar results

## Slide 76: Previous measurement results
Measurement campaign by Weiler et al:
Transmitter performs beamsteering in 2D (azimuth and elevation)
Receiver is omnidirectional
Weiler, R.J., Keusgen, W., Maltsev, A., Kühne, T., Pudeyev, A., Xian, L., Kim, J. and Peter, M., 2016, April. Millimeter-wave outdoor access shadowing mitigation using beamforming arrays. In Antennas and Propagation (EuCAP), 2016 10th European Conference on (pp. 1-5). IEEE.

## Slide 77: Previous measurement results
Locations 2 and 1

## Slide 78: First location
sidelobe
LOS
building reflection
LOS blocked by human
Line of sight free:
Line of sight blocked:

## Slide 79: Second location
reflected path is much weaker
Line of sight free:
Line of sight blocked:

## Slide 80: Millimeter wave channel is sparse and geometrically predictable
WORTH REPEATING

## Slide 81: BEAmforming

## Slide 82: Beamforming is critical for utilizing sparse mm-wave channels
Link budgets require directionality
Tiny wavelength  compact steerable antenna arrays

## Slide 83: Beamforming basics

## Slide 84: Beamforming
Wave front incident from angle θ reaches elements with different phases The signal reaching neighboring elements will have phase lag of k d sin(θ)
0
1
2
3
N-1
θ
d sin(θ)
. . .
array axis
array normal
wave front
(constant phase planes)
d

## Slide 85: Beamforming
Receive beamforming: multiply by conjugate of phase offsets for constructive reception of signal coming from angle θ
0
1
2
3
N-1
θ
d sin(θ)
. . .
array axis
array normal
d
+
N x signal
. . .

## Slide 86: Beamforming
Transmit beamforming: excite elements with phase offset to generate wave in direction θ
0
1
2
3
N-1
θ
d sin(θ)
. . .
array axis
array normal
d
s
signal
. . .
wave front
(constant phase planes)

## Slide 87: Array pattern (as a function of spatial frequency)
When array is beamformed toward angle θ, what is the signal received from angle θ+Δθ?

## Slide 88: Array pattern (as a function of physical angle)
When array is beamformed toward angle θ, what is the signal received from angle θ+Δθ?

## Slide 89: Array pattern
When array is beamformed toward angle θ, what is the signal received from angle θ+Δθ?

## Slide 90: Array pattern
When array is beamformed toward angle θ, what is the signal received from angle θ+Δθ?

## Slide 91: What we do today Digital Beamforming
DAC
upconvert
DAC
upconvert
DAC
upconvert
…
(1)
(2)
(N)
Today’s systems have a small #antennas
#RF chains can’t keep up with mm-wave array scaling

## Slide 92: In order to scale to large arrays RF beamforming
Single RF chain
Less flexible, more scalable
DAC
upconvert
…
(1)
(2)
(N)
Phase
shift
Phase
shift
Phase
shift

## Slide 93: Quantized RF beamforming
Phase shifter hardware
Simplified by quantizing weight phases to a few bits
Analog Attenuator
2-bit phase control

## Slide 94: We will assume RF beamforming
But hybrid models are worth exploring