## Slide 1: Compressive tracking in mm wave picocells
Upamanyu Madhow
ECE Department
University of California, Santa Barbara

## Slide 2: Collaborators
Dinesh Ramasamy
(now at Uber)
Sriram Venkateswaran
(now at Kumu)
Zhinus Marzi
Maryam E. Rasekh
2012-2014
Babak Mamandipoor
2014-present
Prof. Heather Zheng (U. Chicago)
Yanzi Zhu

## Slide 3: Network context
Can fit very large arrays into picocell base stations
Mobile users move  agile tracking needed
Beams are easily blocked, so must be able to switch
  to alternate paths
  to alternate base stations
Each base station must maintain a path inventory for each user
32x32
8cmx8cm
base station
Picocell
Picocell
base station

## Slide 4: Cellular 1000X via mmwave picocells
10-100X bandwidth (2GHz vs. 20-200 MHz)
100X # antennas in same form factor  pencil beams
  Beamforming gain enables comm. over outdoor ranges
  Reduced interference enables aggressive spatial reuse (100x)
32 x 32
8 x 8 cm2
mmwave picocell architecture
basestation
Picocell
Picocell
Notes: One of the most effective ways to provide this capacity is to use mmwave bands. Over which we can have much larger (up to multiGhz) bandwidth. Also, since the wl are very small, large number of antenna elements could be fit in small form factors and provide highly directive beams. This means we can cover outdoor ranges for cellular nets and since there is much smaller interference one can serve multiple users at the same time-increase spatial reuse factor..

## Slide 5: Need to identify paths on the fly
Blockage
Motion tracking
Realign

## Slide 6: Need hyper-efficient channel tracking
To maintain a robust link despite mobility
Overcome blockage
Interference management to utilize spatial reuse
Handover
…
Picocell
Picocell
Notes: To overcome higher path loss, we need larger more directional arrays. Small wavelength means large arrays are easy to make even on a small base.
For mobile communication, beamforming in direction of link needs frequent discovery (tracking) of direction.
Channel tracking provide an important step toward practical mmwave network

## Slide 7: How rapidly must we track?
How long before direction information expires?
Speed of mobile user
Width of beam
V
W=rθ
θ
Pedestrian V=5 m/s | Update every 40ms
Vehicle V=20 m/s | Update every 10ms
Tracking phase
Communication phase
Tracking phase
10ms
< 1ms (desired)
Notes: The frequency of updating direction information depends on speed of mobile user and beam width (i.e. array size)
How frequent? 12x3/180=.2 radx5=1m
Some simple math:
  Speed is 5-20m/s, beam illumination area is 1m for 12 degree beam at (minimum) distance of 5m
  So it takes traveler 25-100 ms to lose signal (mid-beam to edge)
  Update once every 25-100 ms (10-40 times per second)

## Slide 8: Basic calculations
V
W=rθ
θ
angle between speed
and beam cross section
Tracking overhead?
Approximation under worst-case settings for N x N array
Example: urban picocellular base station tracking a vehicle
Need to update more frequently for larger arrays

## Slide 9: Example designs
4x4
16x16
32x32
Update every 10ms
Update every 5ms
Update every 40ms

## Slide 10: Outline
Motivation and Background
  There is a huge capacity at mmwave band
Path tracking is the key bottleneck
  Shortcomings of conventional approaches
  Compressive estimation a promising alternative
Noncoherent compressive estimation
  Works with off-the-shelf hardware
Evaluation on 60 GHz testbed and simulations

## Slide 11: Conventional direction finding techniques
Exhaustive scanning

## Slide 12: Conventional direction finding techniques
Exhaustive scanning
Does not scale well with # of antennas ( N )
Feedback RSS

## Slide 13: Conventional direction finding techniques
Too much feedback overhead and delay
Does not scale well with # of users
Compromise on range and reliability
✔
Scales well with # of antenna ( log(N) )
Feedback RSS
Hierarchical scanning:

## Slide 14: Compressive sensing: basic concept
Nx1
Kx1
K<<N
Our framework: borrow the idea of pseudorandom projections for channel estimation
Notes: Refer
Develop our own framework but borrow some basic ideas from ..
Classical compressive sensing aims to reconstruct signals
which are sparse in a discrete basis, based on a small number
of projections.
these ideas are extended to compressive estimation,
in which a small number of projections are used to estimate
continuous-valued parameters.

## Slide 15: Mmwave channel model
High dimension
(N)
Sparse
(a few paths)
Notes: Refer
Develop our own framework but borrow some basic ideas from ..
Classical compressive sensing aims to reconstruct signals
which are sparse in a discrete basis, based on a small number
of projections.
these ideas are extended to compressive estimation,
in which a small number of projections are used to estimate
continuous-valued parameters.

## Slide 16: Compressive estimation
  ✔ Overhead (# of beacons) scales as Log(N)
  ✔ scalable with # of users
  ✔ Each user sends only one feedback packet
  ✔ Support coarse phase control (e.g. 2bit)
True freq.
Feedback Y
Feedback Y
Template matching
32 beacons
Z. Marzi, D. Ramasamy and U. Madhow, "Compressive Channel Estimation and Tracking for Large Arrays in
mm-Wave Picocells,” IEEE Journal of Selected Topics in Signal Processing

## Slide 17: #beacons scale logarithmically with #elements
1000 element array can be trained with only 24 beacons
5 μs per beacon
training time < 120 μs
overhead < 1.2 % (once every 10 ms for fast car)
Notes: Target accuracy: beamforming loss below 3 dB with 99% probability

## Slide 18: But todays’s transceivers can only do Noncoherent measurements
Frequency offset between local oscillators at TX and RX
Random phase offset in measurements
Phase of measurements cannot be used!
RSS-only measurements
Feedback |Y|
δ
2δ
3δ

## Slide 19: Noncoherent compressive sensing
--Match (normalized) RSS measurements against expected RSS measurements across “spatial frequencies”
--Noisier for noncoherent, but it still works
True spatial freq.
True spatial freq.
32 beacons
Template matching
32 beacons
Template matching
32 beacons

## Slide 20: Hardware scalability: coarse phase control
Large arrays, limited number of RF chains
Simple RF phase control, for example via delay lines
 severe quantization of beamforming phases
Scanning requires fine-grained control
Compressive approaches works fine with severe phase quantization

## Slide 21: ExperimentS

## Slide 22: Hardware: 60GHz testbed
A pair of
  16x8 antenna array
16x8 antenna
5GHz WiFi
Baseband Board
Thanks: Facebook Terragraph team

## Slide 24: Noncoherent cost function follows the same pattern as exhaustive scan

## Slide 25: Dominant path identified effectively
Single path
Two path (one dominant path 8 dB stronger)
Spatial freq. error
Spatial freq. error
Notes: Mean and 95 percentile

## Slide 26: Sims show effective scaling with array size
Notes: Target accuracy: beamforming loss below 3 dB with 99% probability

## Slide 27: Compressive tracking take-aways
Compressive channel tracking eliminates a key bottleneck to Cellular 1000X (and other mm-wave systems)
  Low overhead
  Scalable with # of users and # of antenna elements
  Compatible with simplified hardware (heavily quantized phases)
Noncoherent compressive estimation works with today’s hardware
  Effective solution demonstrated when there is a single dominant path
Recent result: noncoherent algorithms for multipath channels

## Slide 28: Opens up new system design challenges
Assuming each base station maintains path inventory for nearby mobile users
  How do the base stations coordinate to provide robust connectivity?
  How do the base stations coordinate to provide high throughput and manage interference?
  How do we manage the transport layer?
  What are the implications for backhaul requirements?

## Slide 29: Appendix
Details of compressive scheme

## Slide 30: Estimation problem
Estimate gains and spatial frequencies from compressive measurements
Channel is a sum of a few sinusoids

## Slide 31: Can we use standard compressed sensing?
Picture from plenary
by Prof. R. Baraniuk, ITSoc ‘09
Gains of active frequencies
Fourier Basis
Randomized beamforming weights
Observed
projections
Picture from plenary
by Rich Baraniuk, ISIT 2009
Notes: Suppose that nodes, environment everything is stationary

## Slide 32: Basis mismatch is the problem
Frequencies come from a continuum, not a grid
Sensitivity to Basis Mismatch in Compressed Sensing,
Y. Chi, L. Scharf, A. Pezeshki, R. Calderbank
With standard CS, off-grid frequencies can have large estimation errors
Need compressive estimation in a continuum

## Slide 33: Algorithm
Acquisition
  No knowledge of spatial frequencies whatsoever
Tracking
  Leverage frequency estimate from previous round
  Refine based on new measurements

## Slide 34: Acquisition: Coarse Estimate
Notes: At the beginning, don’t know the number of frequencies or their locations
Maximize the inner product between the observations and the sinusoids over a coarse grid

## Slide 35: Acquisition: Coarse Estimate
Notes: At the beginning, don’t know the number of frequencies or their locations

## Slide 36: Iterative refinements
Given
Freqs:
Gains:
Project out contributions from these frequencies
Coarsely estimate (K+1)th freq
Fix gains:
Refine freqs:
Fix freqs:
Estimate g’s:
Stop when residual energy can be explained by noise: CFAR criterion
Notes: Begin as before: pretend that there is only one frequency. Coarse estimate over 2N grid. Refine g and omega iteratively.

## Slide 37: Simulation Setup
Array on
lamp post

## Slide 38: Within a dB of ideal beamforming

## Slide 39: The need for noncoherent tracking
Phase synchronization not maintained between packets
  Relative phase of measurements is corrupted
  Coherent compressive estimation does not work
Effective measurement model (high SNR approximation)

## Slide 40: Noncoherent compressive tracking (single path)
Noncoherent template matching gives ML estimate under high SNR approximation

## Slide 41: Noncoherent compressive tracking (single path)
True spatial freq.
True spatial freq.
32 beacons
Template matching
32 beacons
Template matching
32 beacons

## Slide 42: What about multiple strong paths?
How do we sort out interference across paths?

## Slide 43: Recent result: Noncoherent can be made almost as efficient as coherent
Details omitted until publication
Experimental results not yet obtained

## Slide 44: Time scale of tracking mobile user

## Slide 45: Time scale of tracking mobile user
3-dB beamwidth of N element array:

## Slide 46: Time scale of tracking mobile user
3-dB beamwidth of N element array: