## Slide 1
mmWave Sensing

## Slide 2: Bringing mmWave sensing to mobile devices
Reusing 60 GHz mobile devices for gesture recognition, localization/tracking, and imaging

## Slide 3: Isn’t this the same as radar? No.
New opportunities: reusing mobile comm devices for sensing
Large-scale phased-array: high directionality and electronic steerability
Ubiquity and portability (similar to PCSmartphone revolution)
New challenges: need a redesign of sensing algorithms
Radios differ from radars
Uncontrolled mobility (different from airborne radar or airport mmWave imager)
Sophisticated reflection environment
Limited bandwidth and low computational capability
More applications in IoT space (wireless health, HCI, etc.)

## Slide 4: mTrack: reusing 60 GHz devices for passive tracking
60GHz laser-like directional beam
❶
Tx
Rx
Pen
Rx2
Flexible beam-steering capability
❷
5mm extremely short wavelength
❸
More diffusive on small objects
❹
* “mTrack: High Precision Passive Tracking Using Millimeter Wave Radios”, Teng Wei, Xinyu Zhang, ACM MobiCom’15

## Slide 5: Targeted use cases
Building new mobile human computer interface through wireless sensing
Turn any surface into interactive virtual touchscreen
Enable a new form of pervasive user-computer interface
Virtual Trackpad
Interactive Display
Wireless transcription

## Slide 6: Key challenge: background reflection
Tx
Rx
Objects in
the background
Background Reflection
Target Reflection
Target movement
Phase of
Received
Signal
Background Dominated
Target movement
Phase of
Received
Signal
Less than 2
Target Dominated
Rx
Background Dominated

## Slide 7: Solution: phase counting and regeneration
Target movement
Phase
Periodicity Pattern of Phase
I (TD)
II (BD)
III (ITM)
Target movement
Phase
Phase
Target movement
0 50 100 150 200 250 300 350
Sample index
3
0
-3
1
0
3
0
-3
3
0
-5
PCR Algorithm
Reducing ITM to BD
Step 1
Periodicity Counting
Step 2
Regeneration
Step 3
Input phase

## Slide 8: mTrack: performance overview
Rx 1
Tx
Rx 2
Drywall
Cabinet
1m⨉1m
10cm
10cm
2m
1.5m
Example trajectory of tracking
Error map over tracking region
Tracking Setup
Result
Achieve cm to mm-level tracking
1cm
3cm

## Slide 9: Application and user study
Experiment Setup
Example word
Recognition Accuracy
Integrate mTrack into word-recognition application
Record hand-writing trace from mTrack
Export and control mouse of a PC
MyScript© Stylus for word detection

## Slide 10: E-Mi: sensing assisted 60 GHz network deployment
Reverse engineering
Predict the channel of arbitrarily located links
Reconstruct environment geometry/reflectivity by sampling radio channel
Forward engineering
* “Facilitating Robust 60 GHz Network Deployment by Sensing Ambient Reflectors”, Teng Wei, Anfu Zhou, Xinyu Zhang, USENIX NSDI’17

## Slide 11: E-Mi: let mmWave radios “see” the environment
Radios: extremely low resolution sensors
Only a few “pixel sensors” (antenna elements)
From a camera’s eyes
From a mmWave radio’s eyes
Tx beam patterns
Rx beam patterns

## Slide 12: Achieving super resolution
Model the environment as a sparse set of geometrical structures
….
Tx beam patterns
Rx beam patterns
Tx
Rx
Reconstruct the structure by tracing back the invisible propagation paths
Recover geometries of each path: AoA, AoD, length

## Slide 13: Example
Example: Sparse reconstruction of an office, using only 10 Rx positions
Tx
8.02m
11.10m
Specular reflectors
diffusive reflector
Centroid of virtual sources
Reflector boundaries

## Slide 14: E-Mi: Sensing-assisted mmWave networking
Reflector-aware multi-AP deployment.
Key question:
For a set of APs in a given environment, how to deploy them optimally so as to maximize the coverage and robustness to blockage?
Solution principle
Reconstructing reflector position via wireless channel measurement
Predict signal strength distribution for an arbitrary deployment
Search for the best topology

## Slide 15: Prototyping and experimental results
2x to 5x higher performance than empirical deployment!
Link capacity distribution
Link capacity reduction under random blockage
2x ~ 5x
E-Mi
E-Mi
50Mbps drop
600~800Mbps drop
Notes: [0:37] Our field tests showed that this approach can increase the average network capacity by 2 to 5 times, compared with empirical approaches that deploy the AP randomly or at corners.
It also makes the network more stable, the median throughput drop after blockage is only around 50 Mbps, in comparison to 600 to 800 Mbps when using empirical approaches.

## Slide 16: The impact of sensing on networking
AT&T’s patented Hetnet Analysis and Resource Planning technology (2013)
“Collected extensive measurement… with the help of a drive test vendor”
“Instead of driving a truck, they push a small-cell testbed on a mobile rack.”
Site survey, or war-driving……
Notes: E-Mi is related with the literature of wireless network planning. That is, determining the best location to place access points or basestations, to achieve the best coverage.
But for many years, conventional network planning schemes require network engineers to move around, carrying radios or even mobile basestations with them, and do blanket measurement.

## Slide 17: The impact of sensing on networking
War-driving is infeasible for mmWave networks
Beam steering + human blockage: infinite combinations!
E-Mi: a rigorous way of mmWave network planning
A computational wireless sensing model for network performance prediction
Many more possibilities: Environment aware beam adaptation; Intelligent reflector placement for wireless data centers; ……
Notes: But for mmWave networks, this becomes infeasible, because there are numerous combinations of beam directions and human blockage patterns, and the test space is impossible to be covered by war-driving.
E-Mi essentially automates this procedure, by allowing the mmWave radios to sense the radio environment by themselves, and predict the network performance by themselves.
It opens up many opportunities to make the mmWave network robust and efficient.

## Slide 18: Mobile mmWave imaging
Estimating object distance, curvature, boundary, and surface material
Fix TX, while moving RX to different locations; both using single-beam
* “Reusing 60 GHz Radios for Mobile Radar Imaging”, Yanzi Zhu, Yibo Zhu, Ben Y. Zhao and Haitao Zheng, ACM MobiCom’15
Use reflected RSS patterns to distinguish object geometries/materials

## Slide 19: Mobile mmWave imaging
Ulysses: leveraging beamforming to improve signal diversity
Moving co-located TX/RX following predefined trajectory
* “Object Recognition and Navigation Using a Single Networking Device”, Yanzi Zhu, Yuanshun Yao, Ben Y. Zhao and Haitao Zheng, ACM MobiSys’17

## Slide 20: Mobile mmWave imaging
Potentials and ultimate goals
Low-cost: < $50 (a typical 802.11ad tri-band NIC)
High-resolution: cm level (possible with large bandwidth and large phased-array)
Ubiquitous: 60 GHz phones/tablets already exist

## Slide 21: References
* “Object Recognition and Navigation Using a Single Networking Device”, Yanzi Zhu, Yuanshun Yao, Ben Y. Zhao and Haitao Zheng, ACM MobiSys’17
* “Reusing 60 GHz Radios for Mobile Radar Imaging”, Yanzi Zhu, Yibo Zhu, Ben Y. Zhao and Haitao Zheng, ACM MobiCom’15
* “Facilitating Robust 60 GHz Network Deployment by Sensing Ambient Reflectors”, Teng Wei, Anfu Zhou, Xinyu Zhang, USENIX NSDI’17
* “mTrack: High Precision Passive Tracking Using Millimeter Wave Radios”, Teng Wei, Xinyu Zhang, ACM MobiCom’15
* “60 GHz Synthetic Aperture Radar for Short-Range Imaging: Theory and Experiments”, B. Mamandipoor, G. Malysa, A. Arbabian, U. Madhow and K. Noujeim, Asilomar, 2014
* “Capturing the Human Figure Through a Wall”, Fadel Adib, Chen-Yu Hsu, Hongzi Mao, Dina Katabi, Fredo Durand, ACM SIGGRAPH Asia, 2015