## Slide 1
Millimeter-Wave Wireless Networking and Sensing
Xinyu Zhang
Department of Electrical and Computer Engineering
University of California San Diego
Associate Professor

## Slide 2
mmWave communication and networking standards

## Slide 3: A Roadmap of mmWave standards
 | Wireless PAN | Wireless LAN | Cellular
Standards (year ratified) | 802.15.3c (2006) | 802.11ad (2012), 802.11ay (?) | 5G NR (?)
Use cases | Cable replacement | Gbps Internet access, cordless computing, mesh networking, wireless data center | Gbps wireless broadband, mobile edge computing, V2X
Spectrum | 60 GHz band (57-64 GHz) | 60 GHz band (57-64 GHz) | 28 GHz band (24.25-29.5 GHz)
Channel bandwidth | 2.16 GHz | 2.16 GHz | ?
Range | Below 10m | 10s of meters | 100s of meters
Rate | 5 Gbps | 7 Gbps | Gbps

## Slide 4: 802.11ad Overview
802.11ad (WiGig)
mmWave “WiFi”, with up to 7 Gbps rate
Arguably the most mature mobile mmWave standard, with many commercial products since 2013
Qualcomm/Intel 802.11ac/ad tri-band adapter
TP-Link 802.11ac/ad tri-band access point
Dell 802.11ad laptop & docking station

## Slide 5: 802.11ad Protocol Stack
Extending 802.11
Common Upper MAC
(Management)
Multi-band Operation (WiGig/ .11ad )
BB & Lower MAC
( 802.11b /a / g /n /ac )
BB & Lower MAC
( WiGig /11.ad )
2.4 GHz
5 GHz
60 GHz

## Slide 6: 802.11ad Usage Models (From standard group)

## Slide 7: 802.11ad PHY Layer
Channelization: up to 4 channels (depending on regulation), each 2.16 GHz
USA, Canada, Korea
Europe
China
Japan
Australia
Unlicensed 60 GHz spectrum bands (Note: FCC further released 64-71 GHz band in 2016).
Support phased-array antenna beamforming (but not MIMO)

## Slide 8: 802.11ad PHY Layer: MCS Levels
Control PHY: Robust, low-rate (27.5 Mbps); for signaling, management and control frames
Data PHY: High-rate
OFDM: Support longer distances (larger delay spread), up to 7 Gbps
Single-carrier (SC): Simpler hardware, more power-efficient, suitable for mobile devices, up to 4.6 Gbps

## Slide 9: 802.11ad: Network Architecture
PCP/AP: Central coordinator in a 802.11ad network
Enhanced 802.11 AP to support directional networking
STA: 802.11ad client (can be mobile)
Topology: Simultaneously support infrastructure and P2P connections

## Slide 10: 802.11ad MAC: Overview
Key functionalities
Association, scheduling, beamforming training, interference management, etc.
Isn’t it the same as the directional MAC 10+ years ago? No!
Much narrower beams (down to a few degrees)
Electronically steerable beams
Stronger attenuation at mmWave frequency (vulnerable to blockage)
Large phased-array with hundreds of antennas, instead of a horn
Need new system design for scalability and robustness!

## Slide 11: 802.11ad MAC: Framing
Beacon interval
Following existing 802.11, all nodes are synchronized in beacon intervals
Beacon interval (BI) = BHI + DTI BHI: training, signaling; DTI: data transmission
Two modes of data transmission CBAP: contention-based access periods; SP: Service periods (TDMA)

## Slide 12: 802.11ad MAC: SP Medium Access
SP: TDMA for directional networking
Can be scheduled between AP and STA, or between two STAs (P2P mode)
Need to be coordinated by the AP
Can be dynamically allocated based on polling mechanism:

## Slide 13: 802.11ad MAC: CBAP Medium Access
CBAP: hybrid TDMA+CSMA/CA for directional networking
Physical carrier sensing: energy or preamble detection
Virtual carrier sensing: directional channel reservation
Virtual carrier sensing
Before transmission, send a directional RTS
Nodes who overhear the directional RTS update the NAV (indicating busy time period)
Imperfect! Deafness and hidden terminal problem.
Other operations, e.g., ACK, backoff, packet aggregation, are similar to 802.11ac

## Slide 14: 802.11ad MAC: CSMA Interference management
CSMA based
Directional carrier sensing
Open problems: hidden terminals & deafness
Studied in ad-hoc directional MAC protocols (~2005), but more challenging due to higher directionality, more beams, and imperfect beam patterns
Deafness problem.

## Slide 15: 802.11ad MAC: TDMA interference management
TDMA based
Each STA periodically builds interference map
Sending interference map to AP
AP coordinates multiple links to avoid interference
Open problem: huge overhead in interference mapping, esp. during mobility

## Slide 16: 802.11ad MAC: TDMA interference management
ATI: exchange resource information
BTI
A-BFT
ATI
ATI slot 1
ATI slot 2
ATI slot L
L slots
Use a request-response protocol to exchange the resource request and allocation information, e.g., which STA should transmit at which SP
…
Request
Response
ACK
AP
STA
STA 1
STA L
Scheduling TDMA slots: decision made in beacon header

## Slide 17: 802.11ad MAC: TDMA interference management
TDMA based
An experiment involving 2 links
Update interference map at either beacon intervals or packet level (fine-grained), or not at all (fixed TDMA)
Interference mapping may be even worse due to huge overhead
A tradeoff between responsiveness and overhead
* S. Sur et al., ACM SIGMETRICS’15

## Slide 18: 802.11ad MAC: multiple AP/PCP networks coexist
PCP/AP clustering
BI timing
One of the APs serves as the synchronization AP
Example with 3 APs

## Slide 19: 802.11ad MAC: Beamforming protocol
Challenge:
A phased-array may have hundreds of beam directions to steer to
The TX&RX must decide on the beam direction of each, to maximize “alignment”, thus maximizing link SNR
802.11ad beamforming
Decision making in BHI (can be updated dynamically during DTI)
Essentially a beam training (selection) process

## Slide 20: 802.11ad MAC: Beamforming training
Basic beamforming training procedure
Sector level sweeping (SLS): quasi-omni beams
Beam Combining (BC): both TX and RX are directional
Multiple sector ID detection (MID): TX quasi-omni, RX directional, or vice versa
Notes: 802.11ad Standard: The standard has three phases[30].
The first stage is called Sector Level Sweep (SLS).
In this stage, the AP transmits in all possible directions,
and the client sets its receiver beam pattern to
a quasi-omnidirectional beam. The process is then repeated
with the AP setting its receiver antenna to quasiomnidirectional
and the client sweeping through all transmit
directions. At the end of this stage, the AP and client
each pick the directions that deliver the largest power.
The second stage is called Multiple sector ID Detection
(MID). This stage repeats the process above but with the
transmit beam set to quasi-omni-directional and the scan
being performed with the receive beam. This stage compensates
for imperfections in the quasi omnidirectional
beams. The third stage is called Beam Combining (BC).
In this stage, each of the best directions at the AP are
tried with each of the directions at the client. Hence,
2 combinations are tested and the combination of transmit
and receive beam directions that deliver the maximum

## Slide 21: Scheduling beamforming training
Training during Beacon Transmission Interval
N frames
PCP/AP broadcasts beacon information in each frame
BTI
A-BFT
ATI
BTI Frame1
BTI Frame2
BTI FrameN
PCP/AP uses different beam patterns in different frames
The beam index in used is encoded in the beacon information
If a STA can decode a certain frame, record the beam index and the received SNR
…
AP

## Slide 22: Scheduling beamforming training
BTI: Complete SLS-Tx beam training from AP to STA
BTI
A-BFT
ATI
BTI Frame1
BTI Frame2
BTI FrameN
…
AP

## Slide 23: Scheduling beamforming training
BTI
A-BFT
ATI
ABFT slot 1
ABFT slot N
ABFT slot M
M slots
STA randomly picks one slot
If 2 STAs choose the same slot, they will collide
…
Beamforming training during A-BFT
Collision is resolved by retry

## Slide 24: Scheduling beamforming training
Beamforming training in A-BFT
BTI
A-BFT
ATI
ABFT slot 1
ABFT slot N
ABFT slot M
Sector SWeep (SSW) frame, SSW-feedback frame, and SSW-ACK frame
STA transmits each SSW using a different beam pattern
The index of beam pattern is encoded into the SSW
SSW 1
SSW 2
SSW K
SSW feedback
…
…
SSW ACK
AP
STA
AP records the beam index and SNR of decodable SSW
Notes: Different from BTI: AP receivers, STA sends

## Slide 25: Scheduling beamforming training
BTI
A-BFT
ATI
ABFT slot 1
ABFT slot N
ABFT slot M
SSW 1
SSW 2
SSW K
…
…
SSW ACK
AP
STA
Feedback the best SLS-Tx beam from STA-to-AP
A-BFT: Complete SLS-Tx beam training from STA to AP
SSW feedback

## Slide 26: Scheduling beamforming training in DTI
SLS (optional)
SLS-Rx AP
SLS-Rx STA
BRP-Tx AP
BRP-Tx STA
BRP-Rx AP
BRP-Rx STA
Grant
SSW
AP
STA
Rx-Req
TRN-R fields
TRN-R fields
TRN-T fields
TRN-T fields
Feedback-SNR
Feedback-SNR
SSW
SSW
SSW
SSW
SSW
Indicate whether to do SLS, and how many slots
- SLS-Rx AP
- SLS-Rx STA
- BRP-Tx AP
- BRP-Tx STA
Tx-Req
Tx-OK
Feedback-SNR
- BRP-Rx AP
- BRP-Rx STA
Rx-Req
Tx-Req
Feedback-SNR
Tx-OK
Feedback-SNR
BRP (optional)
Notes: A BRP transaction evaluates a set of directional transmit or receive patterns against the best known directional configuration at the pairing node.

## Slide 27: 802.11ad MAC: Fast Session Transfer (FST)
Seamless switching between 60 GHz 802.11ad and 2.4/5 GHz 802.11n/ac
These three bands share the same MAC address, so channel switching is transparent to higher layers
A request/response protocol is needed between the FST initiator and responder (w/ overhead!)

## Slide 28: Beyond 802.11ad: 802.11ay
Core techniques
Bandwidth aggregation: up to 4x channel bandwidth over 802.11ad
mmWave MIMO and MU-MIMO: up to 4 streams
Next-generation mmWave network standard; full draft expected to be released in 2017
Performance
Bit-rate: up to 44 Gbps with bandwidth aggregation, and 176 Gbps with MIMO

## Slide 29: Beyond 802.11ad: 802.11ay
Wireless VR
Targeting demanding use cases
Inter-rack connectivity for wireless data centers
Video/mass-data distribution in: trains, airplanes, classrooms…

## Slide 30: Experimental research in mmWave networking: beyond the standards
Some existing platforms: open-source software-radios
Key challenge is a programmable platform with phased-array
WiMi 1.0, 2015
OpenMili, 2016
* “60 GHz Indoor Networking through Flexible Beams: A Link-Level Profiling ”, Sanjib Sur, Vignesh Venkateswaran, Xinyu Zhang, Parameswaran Ramanathan, ACM SIGMETRICS’15
* “OpenMili: A 60 GHz Software Radio Platform With a Reconfigurable Phased-Array Antenna ”, Jialiang Zhang, Xinyu Zhang, Pushkar Kulkarni, Parameswaran Ramanathan, ACM MobiCom’16

## Slide 31: Experimental research in mmWave networking: beyond the standards
Some existing platforms: proprietary 802.11ad radios
* “WiFi-Assisted 60 GHz Networks”, Sanjib Sur, Ioannis Pefkianakis, Xinyu Zhang, Kyu-Han Kim, ACM MobiCom’17
* “Object Recognition and Navigation Using a Single Networking Device”, Yanzi Zhu, Yuanshun Yao, Ben Y. Zhao and Haitao Zheng, ACM MobiSys’17

## Slide 32: References
* “WiGig and IEEE 802.11ad For Multi-Gigabyte-Per-Second WPAN and WLAN”, Sai Shankar N., Debashis Dash, Hassan El Madi, Guru Gopalakrishnan, arXiv:1211.7356
* “IEEE 802.11ad: directional 60 GHz communication for multi-Gigabit-per-second Wi-Fi”, Thomas Nitsche ; Carlos Cordeiro ; Adriana B. Flores ; Edward W. Knightly ; Eldad Perahia ; Joerg C. Widmer, IEEE Comm Magazine, 2014
* “WiFi-Assisted 60 GHz Networks”, Sanjib Sur, Ioannis Pefkianakis, Xinyu Zhang, Kyu-Han Kim, ACM MobiCom’17
* “Millimeter Wave Wireless Communications”, Theodore S. Rappaport, Robert W. Heath, Jr., Robert C. Daniels, James N. Murdock, Prentice Hall, 2015
* “60 GHz Indoor Networking through Flexible Beams: A Link-Level Profiling ”, Sanjib Sur, Vignesh Venkateswaran, Xinyu Zhang, Parameswaran Ramanathan, ACM SIGMETRICS’15
* “Demystifying 60GHz Outdoor Picocells”, Yibo Zhu, Zengbin Zhang, Zhinus Marzi, Chris Nelson, Upamanyu Madhow, Ben Y. Zhao, and Haitao Zheng, ACM MobiCom’14